Task II: Study the “of_tutorial” Controller
(A)The function call graph of the controller is as follows:

2(b)
Command:h1 ping -c100 h2
Output:
--- 10.0.0.2 ping statistics ---
100 packets transmitted, 100 received, 0% packet loss, time 99146ms
rtt min/avg/max/mdev = 1.430/24.591/50.828/14.229 ms
The average time to ping from h1→h2 is 24.591ms.

Command:h1 ping -c100 h8
Output:
10.0.0.8 ping statistics ---
100 packets transmitted, 100 received, 0% packet loss, time 99136ms
rtt min/avg/max/mdev = 6.520/29.349/54.875/14.382 ms
The average time to ping from h1→h8 is 29.349 ms.

What is the difference, and why?
Ping is able to calculate the round-trip time by storing the time at which it sends the echo request in the data portion of the ICMP message. The average is the time difference between the ICMP echo request and its echo reply. As h1 is near to h2 than h8,the average time for h8 is more than h2.

iperf is a simple, open source tool to measure the network bandwidth. .
Command: iperf h1 h2
Output:
*** Iperf: testing TCP bandwidth between h1 and h2
.*** Results: ['11.4 Mbits/sec', '13.3 Mbits/sec']

 Command: iperf h1 h8
Output:
*** Iperf: testing TCP bandwidth between h1 and h8
*** Results: ['5.54 Mbits/sec', '6.81 Mbits/sec']

What is the difference, and why?
The throughput(bandwidth) of h1→h2 is more than the throughput(bandwidth) of h1→h8.As the throughput that can be measured with iperf is low compared to the link capacities of core networks.

Task III: MAC learning controller

3(A) Allows the switch to learn the MAC addresses in the network to identify which port to send the traffic to.

Pseudo-­‐code for the MAC learning	switch is as follows:
For every input packet
i. Parse	the packet
ii. Determine the source and	destination MAC addresses.
iv. Check if destination mac address	is mapped to a port.
v. If mapping is found ,send the packet to that port.
vi. If mapping is not	found	flood	it like hub.

Command: h1 ping h2
Output: 132 packets transmitted and 132 received, time is 134122ms.

3(B) Command:h1 ping -c100 h2
        Output:100 packets transmitted,100 packets received,time is 101355ms.The average rrt is	0.052.

       Command:h1 ping -c100 h8
        Output:100 packets transmitted,100 packets received,time is 101332ms.The average rrt is	0.073.

Any difference from Task II (the hub case)?

The rrt time is more for switch than hub. Switches, are capable of determining the destination of each individual traffic element and selectively forwarding data to the one computer that actually needs it. By generating less network traffic in delivering messages, a switch performs better than a hub on busy networks.
3(C)Command:iperf h1 h2
        Output:The TCP bandwidth between h1 and h2 is 35.1 Gbits/sec

       Command: iperf h1 h8
       Output:	The TCP bandwidth between h1 and h8 is 29.8 Gbits/sec.

What is the difference from Task II?
The bandwidth provided by switch is more than hub. The switch determines where the traffic needs to go and transmits it only on the port connected to the destination computer. This is a much more efficient use of the network’s bandwidth, and it also prevents unauthorized users from intercepting traffic on the network.

4(a)Command:h1 ping -c100 h2
       Output:100 packets transmitted,100 packets received,time is 101342ms.The average rrt is	0.051ms.

     Command:h1 ping -c100 h8
       Output:100 packets transmitted,100 packets received,time is 101382ms.The average rrt is	0.071ms.

     Any difference from Task III?
      Not much difference.

4(b) Command:iperf h1 h2
       Output:The TCP bandwidth between h1 and h8 is 40.1 Gbits/sec.

     Command:iperf h1 h8
       Output:The TCP bandwidth between h1 and h8 is 30.9Gbits/sec.

      What is the difference from Task III?
       The bandwidth provided by switch with OpenFlow rules is more in each case.

4(c) The results become better. With OpenFlow, one can tell a switch to match on any field and apply an action. When a new flow comes into the switch, the OpenFlow switch, does a lookup in the flow tables. If no match for the flow is found, the switch creates an OFP packet-in packet and fires it off to the controller for instructions

4(d) Pingall to verify connectivity: